## Slide 1: Spatial: A Language and Compiler for Application Accelerators
David Koeplinger
Matthew Feldman | Raghu Prabhakar | Yaqi Zhang | Stefan Hadjis | Tian Zhao
Ruben Fiszel | Luigi Nardi | Ardavan Pedram | Christos Kozyrakis | Kunle Olukotun
Notes: The Four Components of Big Data Analytics
Big data analytics is the process of examining large data sets to uncover hidden patterns and unknown correlations to accelerate scientific discovery or market trends and customer preferences to develop business insights. This talk will describe four of the key components of big data analytics (1) Extraction Transform and Load (ETL) which takes unstructured data and translates it to structured (tabular) data, (2) Query processing which executes queries over structured data (3) Graph analytics for exploring complex relationships in big data, and (4) Machine learning for building statistical models from big data. For each of the four components we will look at example applications, examine the computational and memory access behavior of the core algorithms and understand how well heterogeneous hardware architectures (CPU, GPU, clusters) perform on these algorithms. This understanding will be used to determine how the hardware for future big-data systems should be architected.

## Slide 2: Spatial Resources
Language documentation and tutorials:
  spatial.stanford.edu
Spatial Google Group:
  groups.google.com/forum/#!forum/spatial-lang-users
Spatial Github Repo:
  github.com/stanford-ppl/spatial-lang
Notes: Improve motivation here – story is (essentially):
1. Why do you want FPGAs/CGRAs?
2. Why is it hard to get them currently?
Also add slide showing where Spatial fits into DAWN flow

## Slide 3: Increasing Demand for Reconfigurability
There is growing demand for reconfigurable architectures as application accelerators in data centers for performance and energy efficiency
Notes: Improve motivation here – story is (essentially):
1. Why do you want FPGAs/CGRAs?
2. Why is it hard to get them currently?
Also add slide showing where Spatial fits into DAWN flow

## Slide 4: Improvements in Performance, Energy Efficiency
                Software Defined Accelerators for DNNs
                Distributed real-time deep learning on FPGAs
                [HotChips ‘14]
                XPU: Programmable FPGA Accelerator
                [HotChips ‘17]
                Project Brainwave
                Distributed real-time deep learning on FPGAs
                [HotChips ‘17]
                Catapult “Configurable Cloud”
                Distributed application and network acceleration
                “…already been deployed at hyperscale and is how
                most new Microsoft data center servers are configured.” [Caulfield et. al. Micro ’16]
                ~10x perf vs. CPU
                ~ 9x perf/W vs. CPU
                2 – 4x perf vs. CPU/GPU
                2 – 3x perf/W vs. CPU/GPU
                CGRA for Parallel Patterns
                [ISCA ‘17]
                Up to 95x perf vs. FPGA
                Up to 75x perf/W vs. FPGA
                64x perf vs. CPU
                25x perf/W vs. CPU

## Slide 5: Accessing Reconfigurable Architectures
Applications
Reconfigurable
Architectures
Performance
Productivity
Efficiency

## Slide 6: Accessing Reconfigurable Architectures
Spatial
Applications
Reconfigurable
Architectures
Performance
Productivity
Efficiency

## Slide 7: Key Programming Challenges
Pipeline timing
  Fine-grained timing of control signals
  Management of multiple clock domains
Disjoint memory spaces
  No hardware-managed cache
  Requires manual data partitioning and timing of memory operations
Limited compute and memory resources
Huge parameter design spaces
  Grows exponentially - even relatively small designs can have very large spaces
  Parameters are interdependent and can change runtime by orders of magnitude
  Manual exploration is tedious and usually suboptimal

## Slide 8: Key Programming Challenges (Continued..)
Quick verification
  Hardware synthesis is too slow to be part of the debug loop
  Writing test benches is challenging and requires waveform debugging
Managing host-accelerator interface
  Tile transfers, register interfaces, data streams, etc.
Incorporating IP cores into design

## Slide 9: Design Space Example
Key
DRAM
A
B
FPGA
+
×
Tile B
Tile A
Small and simple, but slow!
acc
Scratchpad
Reg
op
Algorithm: Dot Product of Vectors A and B

## Slide 10: Important Parameters: Tile Sizes
DRAM
A
B
Increases length of DRAM accesses Runtime
Increases exploited spatial locality Runtime
Increases local memory sizes Area
FPGA
+
×
Tile B
Tile A
Algorithm: Dot Product of Vectors A and B
acc
Key
Scratchpad
Reg
op
Key
Scratchpad
Reg
op

## Slide 11: Important Parameters: Pipelining
DRAM
A
B
FPGA
Stage 2
Stage 1
+
×
Tile B
Tile A
Algorithm: Dot Product of Vectors A and B
Overlaps memory and compute Runtime
Increases local memory sizes Area
Adds synchronization logic Area
acc
Key
Double
Buffer
Reg
op

## Slide 12: Important Parameters: Parallelization
DRAM
FPGA
+
×
Algorithm: Dot Product of Vectors A and B
×
×
Tile A
Tile B
+
+
Improves element throughput Runtime
Duplicates compute resources Area
A
B
acc
Key
Scratchpad
Reg
op
Notes: add legends

## Slide 13
DRAM
FPGA
+
×
Algorithm: Dot Product of Vectors A and B
×
×
Tile A
Tile B
+
+
Improves element throughput Runtime
May duplicate memory resources Area
A
B
acc
Key
Scratchpad
Reg
op
Important Parameters: Memory Banking
Notes: add legends

## Slide 14: Language Requirements
Performance
Productivity
Portability
Performs hardware optimizations for higher level frameworks
Productive language for “power” users (hardware programmers)
Produces efficient hardware

## Slide 15: Language Comparisons
Performance
Productivity
Portability
HDLs (Verilog, VHDL, Chisel, etc.)
High Level Synthesis (C, OpenCL)
Performance
Productivity
Portability
Spatial
Performance
Productivity
Portability
✓ Arbitrary RTL
✘ No high-level
abstractions
✘ No memory
hierarchy
✘ No arbitrary
pipelining
✓ Nested loops
✘ Difficult to tune
✓ Nested loops
✓ Automatic memory banking/buffering
✓ Automated design tuning
✓ Memory hierarchy
✓ Arbitrary pipelining
✘ Can’t write
arbitrary RTL
✓ Target-generic source
✓ Simple host communication API

## Slide 16
Spatial as an Intermediate Representation
val data = LineBuffer[T](K, in_c)
val row = RegFile[T](K, K)
val weight_RF = RegFile[T](K, K)
weight_RF load w_DRAM(channel, 0::K, 0::K)
Foreach(0 until in_r) { r =>
data load i0_DRAM(channel, r, 0::in_c)
Foreach(0 until in_c) { c =>
Foreach(0 until K){
i => row(i, *) <<= data(i, c)
}
val window = Reduce(0 until K, 0 until K){
(i,j) => row(i,j) * weight_RF(i,j)
}{_+_}
conv_out(r, c) = window.value
}
}
Data-flow graphs converted to spatial hardware architectures
FPGA DRAM
x
x
x
+
Line Buffer
SRAM
Reg
File
Shift Reg
Sliding Window
Computation
Output feeds into next layer
From host DRAM
Applications
Spatial IR
Optimization/
Translation
Delite
CGRAs
FPGAs
Spatial Compiler
Plasticine

## Slide 17: The Spatial Language: Memory Abstractions
val videoIn = StreamIn[RGB]
val videoOut = StreamOut[RGB]
val accum = Reg[Double]
val fifo = FIFO[Float](D)
val lbuf = LineBuffer[Int](R,C)
val pixels = ShiftReg[UInt8](R,C)
val buffer = SRAM[UInt8](C)
val image = DRAM[UInt8](H,W)
buffer load image(i, j::j+C)
out := x + y
buffer gather image(a, 10)
Typed storage templates
Explicit transfers across memory hierarchy
Dense and sparse access
Streaming abstractions
Explicit memory hierarchy

## Slide 18: The Spatial Language: Control Abstractions
FSM[Int]{s => s != DONE }{
case STATE0 =>
Foreach(C by 1){j => … }
case STATE1 => …
Reduce(0)(C by 1){i => … }
}{s => nextState(s) }
Accel { … }
Accel(*) { … }
  Blocking/non-blocking
  interaction with host
Arbitrary state machine / loop nesting with implicit control signals

## Slide 19: The Spatial Language: Design Parameters
Spatial templates capture a variety of design parameters:
val B = 64 (64 → 1024)
val buffer = SRAM[Float](B)
Foreach(N by B){i =>
…
}
val P = 16 (1 → 32)
Reduce(0)(N by 1 par P){i =>
data(i)
}{(a,b) => a + b}
Stream.Foreach(0 until N){i =>
…
}
Implicit/Explicit parallelization factors
Explicit size parameters for stride
and buffer sizes
  Implicit/Explicit control schemes
Foreach(64 par 16){i =>
buffer(i) // Parallel read
}
  Implicit memory banking and buffering schemes for parallelized access
Notes: Parts in italics are optional syntax. Default scheme for FSMs is Sequential, for all others is MetaPipe
Streaming is chaining

## Slide 20: Dot Product in Spatial
FPGA
Outer Reduce
Stage 3
val output = ArgOut[Float]
val vectorA = DRAM[Float](N)
val vectorB = DRAM[Float](N)
Accel {
Reduce(output)(N by B){ i =>
val tileA = SRAM[Float](B)
val tileB = SRAM[Float](B)
val acc = Reg[Float]
tileA load vectorA(i :: i+B)
tileB load vectorB(i :: i+B)
Reduce(acc)(B by 1){ j =>
tileA(j) * tileB(j)
}{a, b => a + b}
}{a, b => a + b}
}
DRAM
A
B
Stage 2: Inner Reduce
Stage 1
+
×
tileB
tileA
acc
output
+
Notes: 0. Initial program written in OptiML
Declaration of off-chip memories
Outer loop of tiled reduction with implicit parallelization and pipelining parameters
Declaration of on-chip memories with explicit buffer size
Explicit loads from off-chip to onchip with implicit parallelization
On-chip reduction loop with implicit parallelization
Loads and inner reduction can be overlapped by outer reduce

## Slide 21: Dot Product in Spatial
FPGA
Outer Reduce
Stage 3
val output = ArgOut[Float]
val vectorA = DRAM[Float](N)
val vectorB = DRAM[Float](N)
Accel {
Reduce(output)(N by B){ i =>
val tileA = SRAM[Float](B)
val tileB = SRAM[Float](B)
val acc = Reg[Float]
tileA load vectorA(i :: i+B)
tileB load vectorB(i :: i+B)
Reduce(acc)(B by 1){ j =>
tileA(j) * tileB(j)
}{a, b => a + b}
}{a, b => a + b}
}
DRAM
A
B
Stage 2: Inner Reduce
Stage 1
+
×
tileB
tileA
acc
output
+
Notes: 0. Initial program written in OptiML
Declaration of off-chip memories
Outer loop of tiled reduction with implicit parallelization and pipelining parameters
Declaration of on-chip memories with explicit buffer size
Explicit loads from off-chip to onchip with implicit parallelization
On-chip reduction loop with implicit parallelization
Loads and inner reduction can be overlapped by outer reduce

## Slide 22: Dot Product in Spatial
FPGA
Outer Reduce
Stage 3
val output = ArgOut[Float]
val vectorA = DRAM[Float](N)
val vectorB = DRAM[Float](N)
Accel {
Reduce(output)(N by B){ i =>
val tileA = SRAM[Float](B)
val tileB = SRAM[Float](B)
val acc = Reg[Float]
tileA load vectorA(i :: i+B)
tileB load vectorB(i :: i+B)
Reduce(acc)(B by 1){ j =>
tileA(j) * tileB(j)
}{a, b => a + b}
}{a, b => a + b}
}
DRAM
A
B
Stage 2: Inner Reduce
Stage 1
+
×
tileB
tileA
acc
output
+
Notes: 0. Initial program written in OptiML
Declaration of off-chip memories
Outer loop of tiled reduction with implicit parallelization and pipelining parameters
Declaration of on-chip memories with explicit buffer size
Explicit loads from off-chip to onchip with implicit parallelization
On-chip reduction loop with implicit parallelization
Loads and inner reduction can be overlapped by outer reduce

## Slide 23: Dot Product in Spatial
FPGA
Outer Reduce
Stage 3
val output = ArgOut[Float]
val vectorA = DRAM[Float](N)
val vectorB = DRAM[Float](N)
Accel {
Reduce(output)(N by B){ i =>
val tileA = SRAM[Float](B)
val tileB = SRAM[Float](B)
val acc = Reg[Float]
tileA load vectorA(i :: i+B)
tileB load vectorB(i :: i+B)
Reduce(acc)(B by 1){ j =>
tileA(j) * tileB(j)
}{a, b => a + b}
}{a, b => a + b}
}
DRAM
A
B
Stage 2: Inner Reduce
Stage 1
+
×
tileB
tileA
acc
output
+
Notes: 0. Initial program written in OptiML
Declaration of off-chip memories
Outer loop of tiled reduction with implicit parallelization and pipelining parameters
Declaration of on-chip memories with explicit buffer size
Explicit loads from off-chip to onchip with implicit parallelization
On-chip reduction loop with implicit parallelization
Loads and inner reduction can be overlapped by outer reduce

## Slide 24: Dot Product in Spatial
FPGA
Outer Reduce
Stage 3
val output = ArgOut[Float]
val vectorA = DRAM[Float](N)
val vectorB = DRAM[Float](N)
Accel {
Reduce(output)(N by B){ i =>
val tileA = SRAM[Float](B)
val tileB = SRAM[Float](B)
val acc = Reg[Float]
tileA load vectorA(i :: i+B)
tileB load vectorB(i :: i+B)
Reduce(acc)(B by 1){ j =>
tileA(j) * tileB(j)
}{a, b => a + b}
}{a, b => a + b}
}
DRAM
A
B
Stage 2: Inner Reduce
Stage 1
+
×
tileB
tileA
acc
output
+
Notes: 0. Initial program written in OptiML
Declaration of off-chip memories
Outer loop of tiled reduction with implicit parallelization and pipelining parameters
Declaration of on-chip memories with explicit buffer size
Explicit loads from off-chip to onchip with implicit parallelization
On-chip reduction loop with implicit parallelization
Loads and inner reduction can be overlapped by outer reduce

## Slide 25: Dot Product in Spatial
FPGA
Outer Reduce
Stage 3
val output = ArgOut[Float]
val vectorA = DRAM[Float](N)
val vectorB = DRAM[Float](N)
Accel {
Reduce(output)(N by B){ i =>
val tileA = SRAM[Float](B)
val tileB = SRAM[Float](B)
val acc = Reg[Float]
tileA load vectorA(i :: i+B)
tileB load vectorB(i :: i+B)
Reduce(acc)(B by 1){ j =>
tileA(j) * tileB(j)
}{a, b => a + b}
}{a, b => a + b}
}
DRAM
A
B
Stage 2: Inner Reduce
Stage 1
+
×
tileB
tileA
acc
output
+
Notes: 0. Initial program written in OptiML
Declaration of off-chip memories
Outer loop of tiled reduction with implicit parallelization and pipelining parameters
Declaration of on-chip memories with explicit buffer size
Explicit loads from off-chip to onchip with implicit parallelization
On-chip reduction loop with implicit parallelization
Loads and inner reduction can be overlapped by outer reduce

## Slide 26: Dot Product in Spatial
FPGA
Outer Reduce
Stage 3
val output = ArgOut[Float]
val vectorA = DRAM[Float](N)
val vectorB = DRAM[Float](N)
Accel {
Reduce(output)(N by B){ i =>
val tileA = SRAM[Float](B)
val tileB = SRAM[Float](B)
val acc = Reg[Float]
tileA load vectorA(i :: i+B)
tileB load vectorB(i :: i+B)
Reduce(acc)(B by 1){ j =>
tileA(j) * tileB(j)
}{a, b => a + b}
}{a, b => a + b}
}
DRAM
A
B
Stage 2: Inner Reduce
Stage 1
+
×
tileB
tileA
acc
output
+
Notes: 0. Initial program written in OptiML
Declaration of off-chip memories
Outer loop of tiled reduction with implicit parallelization and pipelining parameters
Declaration of on-chip memories with explicit buffer size
Explicit loads from off-chip to onchip with implicit parallelization
On-chip reduction loop with implicit parallelization
Loads and inner reduction can be overlapped by outer reduce

## Slide 27: Dot Product in Spatial
FPGA
Outer Reduce
Stage 3
val output = ArgOut[Float]
val vectorA = DRAM[Float](N)
val vectorB = DRAM[Float](N)
Accel {
Reduce(output)(N by B){ i =>
val tileA = SRAM[Float](B)
val tileB = SRAM[Float](B)
val acc = Reg[Float]
tileA load vectorA(i :: i+B)
tileB load vectorB(i :: i+B)
Reduce(acc)(B by 1){ j =>
tileA(j) * tileB(j)
}{a, b => a + b}
}{a, b => a + b}
}
DRAM
A
B
Stage 2: Inner Reduce
Stage 1
+
×
tileB
tileA
acc
output
+
Tile Size (B)
Banking strategy
Parallelism factor #1
Pipelining toggle
Parallelism factor #3
Parallelism factor #2
Notes: 0. Initial program written in OptiML
Declaration of off-chip memories
Outer loop of tiled reduction with implicit parallelization and pipelining parameters
Declaration of on-chip memories with explicit buffer size
Explicit loads from off-chip to onchip with implicit parallelization
On-chip reduction loop with implicit parallelization
Loads and inner reduction can be overlapped by outer reduce

## Slide 28: Design Tuning Performance
Benchmark | Designs | Search Time
Dot Product | 5,426 | 5.3 ms / design
Outer Product | 1,702 | 30 ms / design
TPCHQ6 | 5,426 | 8.2 ms / design
Blackscholes | 572 | 27 ms / design
Matrix Multiply | 70,740 | 11 ms / design
K-Means | 75,200 | 20 ms / design
GDA | 42,800 | 17 ms / design
 | Designs | Search Time
GDA | 250 | 1.85 min / design
Vivado HLS:
6500x Speedup Over HLS!
Spatial:
Notes: Add comparison with Vivado HLS exploration time, 6533x speedup

## Slide 29: GDA Design Space
20% 60% 100% 20% 60% 100% 20% 60% 100%
LUTs DSPs BRAMs
Resource Usage (% of maximum)
Cycles (Log Scale)
1010
109
108
107
Valid design point Pareto-optimal (ALMs/cycles) design
Invalid design point Synthesized pareto design point
Performance limited by available BRAMs
Space for GDA spans
four orders of magnitude
Notes: Other benchmarks: 2 – 4 orders of magnitude across resource usage spectrum
ALMS: adaptive logic modules

## Slide 30
Chisel
Bitstream
Preview: TensorFlow to Spatial
val data = LineBuffer[T](K, in_c)
val row = RegFile[T](K, K)
val weight_RF = RegFile[T](K, K)
weight_RF load w_DRAM(channel, 0::K, 0::K)
Foreach(0 until in_r) { r =>
data load i0_DRAM(channel, r, 0::in_c)
Foreach(0 until in_c) { c =>
Foreach(0 until K){
i => row(i, *) <<= data(i, c)
}
val window = Reduce(0 until K, 0 until K){
(i,j) => row(i,j) * weight_RF(i,j)
}{_+_}
conv_out(r, c) = window.value
}
}
Data-flow graphs converted to spatial hardware architectures
FPGA DRAM
x
x
x
+
Line Buffer
SRAM
Reg
File
Shift Reg
Sliding Window
Computation
Output feeds into next layer
From host DRAM
Application
Hierarchical dataflow
graph of tiled pipelines
with memory hierarchy
Spatial IR
Synthesis Tools
Synthesizable
hardware design
Input Data
Conv
Weight
Sum
Pool
Norm
Weight
Conv
Dataflow graph of
domain-specific operators
Scripted
Optimizations
+ Translation
val data = LineBuffer[T](K, in_c)
val row = RegFile[T](K, K)
val weight_RF = RegFile[T](K, K)
weight_RF load w_DRAM(channel, 0::K, 0::K)
Foreach(0 until in_r) { r =>
data load i0_DRAM(channel, r, 0::in_c)
Foreach(0 until in_c) { c =>
Foreach(0 until K){
i => row(i, *) <<= data(i, c)
}
val window = Reduce(0 until K, 0 until K){
(i,j) => row(i,j) * weight_RF(i,j)
}{_+_}…
Spatial
DRAM
Shift Reg
Line Buffer
Reg File
+
SRAM
x
x
x
Delite
Spatial Compiler
Each node in the DFG has a corresponding optimized Spatial template
Cross-node communication uses SRAM and registers to minimize DRAM bandwidth

## Slide 31: Preview: TensorFlow to Spatial
Benefits
  Makes Spatial easier to program
  Automatically benefit from TensorFlow optimizations (e.g. constant folding, fusion, quantization for low precision)
Current support:
  Convolutional Neural Networks
  Recurrent Neural Networks (GRU, LSTM)
  General matrix algebra computations
Same DFG mapping can be applied to other front-ends
  Not specific to TensorFlow

## Slide 32: Spatial’s Advantages
Automatic Design-Space Exploration
  Parallelization selection to balance pipelines
  Tile size selection to balance on-chip memory, bandwidth
Automatic memory banking
Agnostic to hardware vendor, Cloud/Embedded, FPGA/CGRA
Preliminary results: within 20% of DNNWeaver (DNN hardware library)
  For inferences/s of a small network (LeNet) on the Zynq ZC702
  Ongoing work to close 20% gap by further optimizing templates

## Slide 33: Future Work
Unify and support more frontends above Spatial
Expand set of optimizations done by Spatial compiler
Expand backends supported by Spatial
Low precision DNN training
Residual Networks
Applications
Spatial IR
Optimization/
Translation
Delite
CGRAs
FPGAs
Spatial Compiler
Plasticine
DSE
Optimizer

## Slide 34: Conclusion
Orders of magnitude improvements in performance and energy efficiency are possible with reconfigurable architectures
Spatial’s intermediate representation can be used as a bridge to reconfigurable architectures
The Spatial language includes abstractions for performance, productivity, and portability
Spatial’s design tuning is ~6500x faster than that possible with Vivado HLS
Preliminary results within 20% of manual HDL on CNN implementations
Productivity
Portability
Performance
We’re always looking for new users and feedback!
Open source at: spatial.stanford.edu

## Slide 35: Nuts and Bolts of a Full Spatial Application
Continue to see the bird’s eye view of how to write a full application
Visit the website tutorial for more detailed examples:
  http://spatial-lang.readthedocs.io/en/latest/tutorial/starting.html

## Slide 36: Spatial App Template
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
AppName
ARM Host Code (setup)
FPGA Code
ARM Host Code (teardown)

## Slide 37: Spatial App Template
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
AppName
Define FPGA peripherals
Send data from ARM to FPGA
- Define FPGA operations
- Get data from the FPGA

## Slide 38: Hello Spatial!
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 39: Spatial is Embedded in Scala
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
Spatial can be thought of as a Scala library
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 40: Spatial is Embedded in Scala
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
Semicolons are optional
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 41: Import Statements
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Same in every Spatial program
(Similar idea to #include in C,
Identical to import in Java, Python)

## Slide 42: Import Statements
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
Spatial-specific classes
(primarily SpatialApp)
1
2
3
4
5
6
7
8
Useful macros for nicer syntax (more later)

## Slide 43: Application Object Declaration
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Spatial applications are always objects

## Slide 44: Application Object Declaration
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Name of application
All Spatial applications inherit from (“extends”) SpatialApp

## Slide 45: “@virtualize” Annotation
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
All functions in Spatial should have this annotation
(Allows overloading Scala constructs like if-then-else)

## Slide 46: Spatial’s Entry Function: “main()”
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Spatial’s entry function

## Slide 47: Spatial’s Entry Function: “main()”
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Starts a function declaration
Function return type
(Unit: same as void)

## Slide 48: Val Definitions
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Declares an immutable value named
“input” (value can’t be modified later)

## Slide 49: Val Definitions
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input: Int = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Value types are optional in Scala.

## Slide 50: Val Definitions
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Scala is statically typed (like C, Java)
Without the “: Int”, the type of this value is inferred by the compiler.

## Slide 51: Method Calls
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Round brackets ( ) for value parameters
Square brackets [ ] are for type parameters

## Slide 52: Spatial Command-Line Arguments
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Spatial app’s command-line arguments
Conversion from String to Int
int main(int argc, char **argv) {
int in = atoi(argv[1]);
printf(“Output: %d\n", out);
return 0;
}
ARM
FPGA
+
4
out
in

## Slide 53: Input Arguments (ArgIn)
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Creates a new register to capture a scalar argument from the ARM
ARM
FPGA
+
4
out
in

## Slide 54: Output Arguments (ArgOut)
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Creates a new scalar argument to the ARM from the FPGA
ARM
FPGA
+
4
out
out
in

## Slide 55: Scalar Transfers (ARM → FPGA)
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Tells the host ARM to write input to scalar argument in on the FPGA
ARM
FPGA
+
4
out
in
input

## Slide 56: Accel Block
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
FPGA
ARM
+
4
out
in
Defines an FPGA computation scope. Everything in here goes on the FPGA

## Slide 57: Accel Block
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
FPGA
ARM
+
4
out
in
The types of operations that can be done in this scope are limited to synthesizable Spatial

## Slide 58: Accel Block
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
FPGA
ARM
+
4
out
in
Accel handles control signals for you.
It implicitly creates:
- a start signal (ARM → FPGA)
- a done signal (FPGA → ARM)
start
done

## Slide 59: Implicit Register Reads
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
ARM
FPGA
+
4
out
in
Implicitly creates a wire from the register (ArgIn) in

## Slide 60: Register Writes
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
ARM
FPGA
+
4
out
in
:= creates a write of the value
in + 4 to the register out

## Slide 61: Accel Block Scheduling
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
FPGA
ARM
+
4
out
in
Accel guarantees that FPGA execution completes after all operations in this block complete
done

## Slide 62: Scalar Transfers (FPGA → ARM)
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
ARM
FPGA
+
4
out
in
Gets the value of the ArgOut out
from the FPGA back to the ARM

## Slide 63: Printing in Spatial**
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Prints the output to the terminal
int main(int argc, char **argv) {
int in = atoi(argv[1]);
…
printf(“Output: %d\n", out);
return 0;
}
ARM
FPGA
+
4
out
in
** Printing in Spatial isn’t synthesizable,
but it can be used in host code and in
debugging (more in future lectures)

## Slide 64: Hello Spatial!
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 65: Custom Types in Spatial
Now what if we want an ArgIn value that isn’t an Int?
Other options:
  Custom fixed point types
  Custom floating point types
  Structs
  Vectors

## Slide 66: Custom Types
val input = args(0).to[Int]
val in = ArgIn[Int]
setArg(in, input)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 67: Custom Fixed Point Types
type Q8_8 = FixPt[FALSE,_8,_8]
val input = args(0).to[Int]
val in = ArgIn[Int]
setArg(in, input)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
TRUE = Signed
FALSE = Unsigned
_N = # of integer bits
(N from 1 to 128)
_N = # of fraction bits
(N from 0 to 128)
0b00000000.00000000
Integer bits
Fraction bits

## Slide 68: Custom Fixed Point Examples
type Q8_8 = FixPt[FALSE,_8,_8]
type UInt8 = FixPt[FALSE,_8,_0]
type LongLong = FixPt[TRUE,_128,_0]
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
0b00000000.00000000
Integer bits
Fraction bits

## Slide 69: Custom Fixed Point Types
type UInt8 = FixPt[FALSE,_8,_0]
val input = args(0).to[UInt8]
val in = ArgIn[UInt8]
setArg(in, input)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 70: Custom Floating Point Types
type Float = FltPt[_23,_11]
val input = args(0).to[Int]
val in = ArgIn[Int]
setArg(in, input)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
_N = # of significand bits + 1
(N from 1 to 128)
Includes sign bit!
_N = # of exponent bits
(N from 0 to 128)
0 00000000 x 2^00000000
Significand bits
Exponent bits
Sign bit

## Slide 71: Custom Floating Point Types
type Half = FltPt[_11,_5]
val input = args(0).to[Half]
val in = ArgIn[Half]
setArg(in, input)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 72: Predefined Type Aliases
type Char = FixPt[TRUE,_8,_0]
type Short = FixPt[TRUE,_16,_0]
type Int = FixPt[TRUE,_32,_0]
type Long = FixPt[TRUE,_64,_0]
type Half = FltPt[_11,_5] // 754 Half
type Float = FltPt[_24,_8] // 754 Single
type Double = FltPt[_53,_11] // 754 Double
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 73: Note About Booleans
val input = args(0).to[Boolean]
val in = ArgIn[Boolean]
setArg(in, input)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Note: For API purposes,
Boolean is NOT the same as single bit fixed point number
Uses “false” and “true”
rather than 0 and 1

## Slide 74: Custom Structs
@struct class MyStruct(
red: Int,
green: Int,
blue: Int
)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Declares a new Struct type with the given list of fields

## Slide 75: Custom Structs
@struct class MyStruct(
red: Int,
green: Int,
blue: Int
)
val bus = MyStruct(147, 192, 125)
1
2
3
4
5
6
7
8
9
10
11121314
15
16
17
18
Allocates an instance of the struct.
Note: NO new keyword used
147
192
125
32
32
32
96
bus
In hardware, a struct instance is just a concatenation of wires

## Slide 76: Custom Structs
@struct class MyStruct(
red: Int,
green: Int,
blue: Int
)
val bus = MyStruct(147, 192, 125)
val red = bus.red
val blue = bus.blue
1
2
3
4
5
6
7
8
9
10
11121314
15
16
17
18
Creates a reference to the struct field (equivalent to a bit slice)
147
192
125
32
32
32
96
bus
32
red
blue

## Slide 77: Custom Structs
@struct class MyStruct(
red: Int,
green: Int,
blue: Int
)
val bus = MyStruct(147, 192, 125)
bus.blue = 45
1
2
3
4
5
6
7
8
9
10
11121314
15
16
17
18
Note: Allocated structs are immutable!
We can’t write to them or change the contents!
147
192
125
32
32
32
96
bus

## Slide 78: Nesting Structs
@struct class RGB(
red: Int,
green: Int,
blue: Int
)
@struct class RGBA(
rgb: RGB,
alpha: Int
)
1
2
3
4
5
6
7
8
9
10
11121314
15
16
17
18

## Slide 79: Registers of Custom Types
@struct class MyStruct(
red: Int,
green: Int,
blue: Int
)
val in = ArgIn[MyStruct]
in.red
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Creates an ArgIn register which holds a value of type MyStruct
Note: Registers can hold structs as long as the fields are primitive values (FixPt, FltPt, Boolean) or other primitive-based structs