## Slide 1: Spatial Tutorial
Part 1: Introduction to Spatial

## Slide 2: Spatial Resources
Language documentation and tutorials: spatial.stanford.edu
Spatial Google Group: groups.google.com/forum/#!forum/spatial-lang-users
Spatial Github Repo: github.com/stanford-ppl/spatial-lang

## Slide 3: Introduction

## Slide 4: Hardware Accelerator Design
Hardware accelerators?
What is involved in designing one?

## Slide 5: Simple Example: ARM (CPU Host)
Add '4' to an input integer
int main(int argc, char **argv) {
int in = atoi(argv[1]);
int out = in + 4;
printf(“Output: %d\n”, out);
return 0;
}
ARM A9
(Host)
DRAM

## Slide 6: Simple Example: ARM A9 (Host)
Add '4' to an input integer
int main(int argc, char **argv) {
int in = atoi(argv[1]);
int out = in + 4;
printf(“Output: %d\n”, out);
return 0;
}
ARM A9
(Host)
in
out

## Slide 7: Simple Example: ARM + FPGA
Perform addition on FPGA
// Host Code: C
??
// FPGA Code: Verilog
??
ARM A9
(Host)
CPU DRAM
FPGA
(Accelerator)
FPGA DRAM

## Slide 8: Simple Example: ARM + FPGA
Add '4' to an input integer
// FPGA Code: Verilog
// 1. Write addition module
module add4(
input wire[31:0] in,
output wire[31:0] out
);
assign out = in + 31’h4;
endmodule
ARM A9
(Host)
CPU DRAM
FPGA DRAM
+
4
in
out

## Slide 9: Simple Example: ARM + FPGA
Add '4' to an input integer
ARM A9
(Host)
CPU DRAM
FPGA DRAM
+
4
r0
r1
in
out
// FPGA Code: Verilog
// 1. Write addition module
// 2. Create registers
regFile #(2) rf(…)

## Slide 10: Simple Example: ARM + FPGA
Add '4' to an input integer
ARM A9
(Host)
CPU DRAM
FPGA DRAM
+
4
r0
r1
in
out
// FPGA Code: Verilog
// 1. Write addition module
// 2. Create registers
// 3. Connect to host bus

## Slide 11: Simple Example: ARM + FPGA
Add '4' to an input integer
ARM A9
(Host)
CPU DRAM
FPGA DRAM
+
4
r0
r1
in
out
// FPGA Code: Verilog
// 1. Write addition module
// 2. Create registers
// 3. Connect to host bus
// Host Code: C
int main(int argc, char **argv) {
int in = atoi(argv[1]);
int out = 0;
// ???
printf(“Output: %d\n", out);
return 0;
}

## Slide 12: Simple Example: ARM + FPGA
Add '4' to an input integer
ARM A9
(Host)
CPU DRAM
FPGA DRAM
+
4
r0
r1
in
out
// FPGA Code: Verilog
// 1. Write addition module
// 2. Create registers
// 3. Connect to host bus
// Host Code: C
int main(int argc, char **argv) {
int in = atoi(argv[1]);
int out = 0;
// Set up MMIO for r0, r1
// Configure FPGA bitstream
// Write ‘in’ to r1
// Write ‘1’ to command reg
// Wait until FPGA status=1 // Read r0 to ‘out’
printf(“Output: %d\n”, out);
return 0;
}

## Slide 13: Simple Example: ARM + FPGA
Add '4' to an input integer
ARM A9
(Host)
CPU DRAM
FPGA DRAM
+
4
r0
r1
in
out
// FPGA Code: Verilog
// 1. Write addition module
// 2. Create registers
// 3. Connect to host bus
// Host Code: C
int main(int argc, char **argv) {
int in = atoi(argv[1]);
int out = 0;
init_fpga();
config_fpga(“add4.bin”)
write_to_fpga(1, in);
run_fpga();
read_from_fpga(0, &out);
printf(“Output: %d\n”, out);
return 0;
}

## Slide 14: Simple Example: In a Nutshell
Program starts on host, offloaded to accelerator
  Interaction with host and peripherals
Hardware data and control path design
  Take advantage of parallelism and locality
  Hierarchical Pipelining, on-chip memory banking, double buffering…
Verification
Requires understanding hw-sw interaction

## Slide 15: Simple Example: Excluded details
How to test/verify code?
  Logic synthesis takes minutes/hours to run, impractical for iterative code-run-debug cycles
  How to write simulation testbenches?
Low-level details
  Instantiating reset controllers and other supporting IP
  Implementing software APIs

## Slide 16: Reality Is More Complicated
ARM A9
(Host)
CPU DRAM
FPGA
FPGA DRAM
Camera
Display
GPIO
…
Ethernet

## Slide 17: Reality Is More Complicated
Hardware Video decoder + UDP ?
ARM A9
(Host)
CPU DRAM
FPGA
FPGA DRAM
Camera
Display
GPIO
…
Ethernet

## Slide 18: Introducing Spatial
Programming language to simplify accelerator design
  Simple APIs to manage Host <-> FPGA communication
  Peripherals exposed as streams i.e.: data, ready, valid
  In-built constructs to express parallel datapaths, on-chip memories etc
  Automatic functional and cycle-accurate simulation
Focus on “interesting stuff” aka accelerator datapath and control design

## Slide 19: Spatial Model
Spatial Compiler
Spatial Code
FPGA Code
gcc
FPGA compiler
ARM A9
FPGA
Host Code

## Slide 20: Spatial Programming Basics

## Slide 21: Spatial App Template
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
AppName
ARM Host Code (setup)
FPGA Code
ARM Host Code (teardown)

## Slide 22: Spatial App Template
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
AppName
Define FPGA peripherals
Send data from ARM to FPGA
- Define FPGA operations
- Get data from the FPGA

## Slide 23: Hello Spatial!
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 24: Spatial is Embedded in Scala
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
Spatial can be thought of as a Scala library
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 25: Spatial is Embedded in Scala
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
Semicolons are optional
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 26: Import Statements
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Same in every Spatial program
(Similar idea to #include in C,
Identical to import in Java, Python)

## Slide 27: Import Statements
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
Spatial-specific classes
(primarily SpatialApp)
1
2
3
4
5
6
7
8
Useful macros for nicer syntax (more later)

## Slide 28: Application Object Declaration
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Spatial applications are always objects

## Slide 29: Application Object Declaration
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Name of application
All Spatial applications inherit from (“extends”) SpatialApp

## Slide 30: “@virtualize” Annotation
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
All functions in Spatial should have this annotation
(Allows overloading Scala constructs like if-then-else)

## Slide 31: Spatial’s Entry Function: “main()”
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Spatial’s entry function

## Slide 32: Spatial’s Entry Function: “main()”
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Starts a function declaration
Function return type
(Unit: same as void)

## Slide 33: Val Definitions
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Declares an immutable value named
“input” (value can’t be modified later)

## Slide 34: Val Definitions
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input: Int = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Value types are optional in Scala.

## Slide 35: Val Definitions
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Scala is statically typed (like C, Java)
Without the “: Int”, the type of this value is inferred by the compiler.

## Slide 36: Method Calls
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Round brackets ( ) for value parameters
Square brackets [ ] are for type parameters

## Slide 37: Spatial Command-Line Arguments
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Spatial app’s command-line arguments
Conversion from String to Int
int main(int argc, char **argv) {
int in = atoi(argv[1]);
printf(“Output: %d\n", out);
return 0;
}
ARM
FPGA
+
4
out
in

## Slide 38: Input Arguments (ArgIn)
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Creates a new register to capture a scalar argument from the ARM
ARM
FPGA
+
4
out
in

## Slide 39: Output Arguments (ArgOut)
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Creates a new scalar argument to the ARM from the FPGA
ARM
FPGA
+
4
out
out
in

## Slide 40: Scalar Transfers (ARM → FPGA)
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Tells the host ARM to write input to scalar argument in on the FPGA
ARM
FPGA
+
4
out
in
input

## Slide 41: Accel Block
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
FPGA
ARM
+
4
out
in
Defines an FPGA computation scope. Everything in here goes on the FPGA

## Slide 42: Accel Block
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
FPGA
ARM
+
4
out
in
The types of operations that can be done in this scope are limited to synthesizable Spatial

## Slide 43: Accel Block
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
FPGA
ARM
+
4
out
in
Accel handles control signals for you.
It implicitly creates:
- a start signal (ARM → FPGA)
- a done signal (FPGA → ARM)
start
done

## Slide 44: Implicit Register Reads
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
ARM
FPGA
+
4
out
in
Implicitly creates a wire from the register (ArgIn) in

## Slide 45: Register Writes
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
ARM
FPGA
+
4
out
in
:= creates a write of the value
in + 4 to the register out

## Slide 46: Accel Block Scheduling
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
FPGA
ARM
+
4
out
in
Accel guarantees that FPGA execution completes after all operations in this block complete
done

## Slide 47: Scalar Transfers (FPGA → ARM)
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
ARM
FPGA
+
4
out
in
Gets the value of the ArgOut out
from the FPGA back to the ARM

## Slide 48: Printing in Spatial**
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Prints the output to the terminal
int main(int argc, char **argv) {
int in = atoi(argv[1]);
…
printf(“Output: %d\n", out);
return 0;
}
ARM
FPGA
+
4
out
in
** Printing in Spatial isn’t synthesizable,
but it can be used in host code and in
debugging (more in future lectures)

## Slide 49: Hello Spatial!
import spatial._
import org.virtualized._
object HelloSpatial extends SpatialApp {
@virtualize
def main(): Unit = {
val input = args(0).to[Int]
val in = ArgIn[Int]
val out = ArgOut[Int]
setArg(in, input)
Accel {
out := in + 4
}
println(“Output: ” + getArg(out))
}
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 50: Custom Types in Spatial
Now what if we want an ArgIn value that isn’t an Int?
Other options:
  Custom fixed point types
  Custom floating point types
  Structs
  Vectors

## Slide 51: Custom Types
val input = args(0).to[Int]
val in = ArgIn[Int]
setArg(in, input)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 52: Custom Fixed Point Types
type Q8_8 = FixPt[FALSE,_8,_8]
val input = args(0).to[Int]
val in = ArgIn[Int]
setArg(in, input)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
TRUE = Signed
FALSE = Unsigned
_N = # of integer bits
(N from 1 to 128)
_N = # of fraction bits
(N from 0 to 128)
0b00000000.00000000
Integer bits
Fraction bits

## Slide 53: Custom Fixed Point Examples
type Q8_8 = FixPt[FALSE,_8,_8]
type UInt8 = FixPt[FALSE,_8,_0]
type LongLong = FixPt[TRUE,_128,_0]
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
0b00000000.00000000
Integer bits
Fraction bits

## Slide 54: Custom Fixed Point Types
type UInt8 = FixPt[FALSE,_8,_0]
val input = args(0).to[UInt8]
val in = ArgIn[UInt8]
setArg(in, input)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 55: Custom Floating Point Types
type Float = FltPt[_23,_11]
val input = args(0).to[Int]
val in = ArgIn[Int]
setArg(in, input)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
_N = # of significand bits + 1
(N from 1 to 128)
Includes sign bit!
_N = # of exponent bits
(N from 0 to 128)
0 00000000 x 2^00000000
Significand bits
Exponent bits
Sign bit

## Slide 56: Custom Floating Point Types
type Half = FltPt[_11,_5]
val input = args(0).to[Half]
val in = ArgIn[Half]
setArg(in, input)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 57: Predefined Type Aliases
type Char = FixPt[TRUE,_8,_0]
type Short = FixPt[TRUE,_16,_0]
type Int = FixPt[TRUE,_32,_0]
type Long = FixPt[TRUE,_64,_0]
type Half = FltPt[_11,_5] // 754 Half
type Float = FltPt[_24,_8] // 754 Single
type Double = FltPt[_53,_11] // 754 Double
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

## Slide 58: Note About Booleans
val input = args(0).to[Boolean]
val in = ArgIn[Boolean]
setArg(in, input)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Note: For API purposes,
Boolean is NOT the same as single bit fixed point number
Uses “false” and “true”
rather than 0 and 1

## Slide 59: Custom Structs
@struct class MyStruct(
red: Int,
green: Int,
blue: Int
)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Declares a new Struct type with the given list of fields

## Slide 60: Custom Structs
@struct class MyStruct(
red: Int,
green: Int,
blue: Int
)
val bus = MyStruct(147, 192, 125)
1
2
3
4
5
6
7
8
9
10
11121314
15
16
17
18
Allocates an instance of the struct.
Note: NO new keyword used
147
192
125
32
32
32
96
bus
In hardware, a struct instance is just a concatenation of wires

## Slide 61: Custom Structs
@struct class MyStruct(
red: Int,
green: Int,
blue: Int
)
val bus = MyStruct(147, 192, 125)
val red = bus.red
val blue = bus.blue
1
2
3
4
5
6
7
8
9
10
11121314
15
16
17
18
Creates a reference to the struct field (equivalent to a bit slice)
147
192
125
32
32
32
96
bus
32
red
blue

## Slide 62: Custom Structs
@struct class MyStruct(
red: Int,
green: Int,
blue: Int
)
val bus = MyStruct(147, 192, 125)
bus.blue = 45
1
2
3
4
5
6
7
8
9
10
11121314
15
16
17
18
Note: Allocated structs are immutable!
We can’t write to them or change the contents!
147
192
125
32
32
32
96
bus

## Slide 63: Nesting Structs
@struct class RGB(
red: Int,
green: Int,
blue: Int
)
@struct class RGBA(
rgb: RGB,
alpha: Int
)
1
2
3
4
5
6
7
8
9
10
11121314
15
16
17
18

## Slide 64: Registers of Custom Types
@struct class MyStruct(
red: Int,
green: Int,
blue: Int
)
val in = ArgIn[MyStruct]
in.red
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Creates an ArgIn register which holds a value of type MyStruct
Note: Registers can hold structs as long as the fields are primitive values (FixPt, FltPt, Boolean) or other primitive-based structs